# DI-304 Installation Guide for LAN – LAN Setup

To configure the router for LAN – LAN, follow the screens setting below.

The router has a default IP address of 192.168.0.1, and is setup as a DHCP server. The PC you will use to configure the DI-304 will need to be setup to receive its IP address from a DHCP server.

Router Main Menu

~ End of Document ~

# Text boxes

Select call direction and idle timeout.

Select 64, 128 or BOD for this connection, and authentication for the dial out settings

Setup the parameters for dial in.

These setting may be left as default.

Give an appropriate name for the profile, and enable it.

Enter the dial out username and password.

If the other router dial this site, then complete the din-in settings.

For unnumbered link leave my WAN IP as 0.0.0.0. The remote gateway in the IP address of the remote router. Enter the remote network and mask.

You can setup 16 LAN-LAN profiles, that is to say you can connect to 16 remote networks. Select an available index.

Select LAN-LAN Dialer Profile Setup

To configure the router, in your WEB browser type the IP address of the router, this will be 192.168.0.1

In the TCPIP properties of your Ethernet adapter, configure it so that the IP address is obtained automatically.